1. Product Feature  IPC3F29EP

 1/4” line scanning digital and advanced DSP technology

 Picture Resolution 720P color CMOS , 1.0 Mega Pixel, 1280X720

 Optimized H.264 Main Profile compression algorithm, high compression ratio and high quality image; convenient to realize a transmission of HD images on a narrow band, thus it can save the storage space; support triple bit streams

 The most advanced network delivery server technology ,Easily achieve more user access , Multi-stage user password rights management

 Built in Web Server， through the IE browser easy to realize the remote control Settings prison see operation

 Support facilities remote security upgrade function

 Support DDNS 、PPPoE and（UPnP），Support Lan 、Wan transport.

 Technology of self adaptability to network that it may adjust its video flame rate automatically according to the bandwidth of network

 Functions of alarm in video missing, mobile detection or probe, etc. (available to set the regions and sensitivity)

 Support mobile detection / image shielding / image snapshot

 Functions of auto recovery in abnormality and auto reconnection in network breakdown

2. Product Specification

|  | Model | AOP-IPC3F29P |
| --- | --- | --- |
| Camera | Pixel | 1.0 Mega Pixel, 1280*720 |
|  | Lens | 3.6mm |
|  | Electronic shutter | 1/25s-1/30,000s |
|  | Low Lux | Color：0.1Lux@F1.6 B/W：0.08Lux@F1.2 |
|  | Auto iris | N/A |
|  | ICR | N/A |
|  | Video parameter | Saturation, brightness, contrast ratio and color tone can be adjusted by customer end or IE explorer |
| IR | IR Properties | N/A |
|  | IR Light | N/A |
| Audio-video coding parameters | Compression | H.264 Main Profile@Level 3.0 / MJPEG optional |
|  | Video bit rate | 0.1M-6Mbps, customized |
|  | Bit stream type | video stream |
|  | Audio compress | N/A |
|  | Audio bit rate | N/A |
|  | Triple bit streams | Support |
| Image | Video resolution | 1280*720 |
|  | Video flame rate | PAL: 1-25 frames/second, NTSC: 1-30 frames/second |
| Function | PTZ | N/A |
|  | Heartbeat mechanism | Support |
|  | IP auto pop-out | IP auto pop-out at customer end |
|  | Password protection | Multi-level protection on password |
|  | Intellectual alarm | Mobile detection, video shielding, video loss, network breakdown, abnormality in storage |
|  | Basic functions | One-key reset, password protection, watermark technology |
| Interface | Audio input | YES |
|  | Video output | N/A |
|  | Network port | 1 pcs, RJ45 10M/100Mbps self-adaptable Ethernet port |
|  | Serial port | N/A |
|  | Alarm input | N/A |
|  | Alarm output | N/A |
| Wireless network | WIFI | N/A |
|  | Wireless encryption protocol | N/A |
|  | Cell phone monitor | Support |
|  | 3G network | N/A |
| others | POE | N/A |
|  | Power supply | DC12V/1.5A |
|  | Power consumption | <6W |
|  | Working temp | -10℃ ~ +55 ℃ |
|  | Working humidity | 10 ~ 85% |
|  | Dimension | L115.58mm*W100.8mm*H45.66mm |
|  | Weight | 0.3Kg |