8CH 4.0MPTVI AHD CVI IP CVBS 5 in 1 XVR

# Features

- 8 channel 4.0MP AHD&TVI&CVI real-time live view

- H.264 & Dual-stream video compression

- Support AHD, TVI, CVI , analog cameras and IP camera

- Support VGA, HDMI HD output

- 8 channel 4.0MP synchronous playback

- Support cloud server

- Multiple network monitoring: Web viewer, CMS & Mobile

Technical Specifications

| HD3808TVI4M-42S |
| --- |
| System |
| Operating System | Embedded LINUX |
| Main processor | Hi3521A |
| System resources | Simultaneous multi-channel recording, playback, network operation, USB backup |
| Video & Audio Input |
| Video Input | 8channel |
| Resolution | Analog+IP camera(PAL): 8 * 4M/6 + 0; 8 * 4M/8 + 0; 4 * 4M/6 + 4 * 4M/25; 0 + 8 * 1080P/25; 0 + 4 * 3M/25; 0 + 4 * 5M/25; |
| Audio input | 4channel, RCA |
| Video input Interface | BNC(1.0Vp-p,75Ω） |
| Video compression | H264 |
| Audio compression | G.711a |
| Bidirectional talk | Support |
| Display |
| Interface | 1 HDMI, 1 VGA |
| User interface | support 16-bit true color graphical menu interface and mouse operation |
| Resolution | 1024*768;1280*720;1280*1024;1440*900;1920*1080; 2560*1440 |
| Display Split | 1/4/8 |
| OSD | Channel title, Time, Video loss, Camera lock, Motion detection, Recording |
| Recording |
| Record Mode | Manual, Auto(Regular(Continuous), MD, Alarm), Off |
| Record Interval | 1~120min (default: 60 min), Pre-record: 1~30sec |
| Alarm |
| Trigger Events | Recording，Alarm，Video Push，Email, Buzzer |
| Video Detection | Motion Detect, Video Blind, Video Loss |
| Abnormal | HDD loss, Low HDD capacity, Net disconnection, IP conflict, HDD error |
| Playback & Backup |
| Sync Playback | 8 * 4M/6; 4 * 4M/8; 2 * 4M/6; 4 * 1080P/25; 4 * 3M/25; 2 * 5M/25; |
| Search Mode | Time/Date, Alarm, MD & Exact search (accurate to second) |
| Playback Functions | Play, Pause, Stop, Rewind, Fast play, Slow play, Next file, Previous file, Next camera, Previous camera, Full screen, Repeat, Shuffle, Backup selection, Digital zoom |
| Backup Mode | USB Device / Network |
| Network |
| Ethernet | RJ-45 port, 10/100M |
| Network Functions | HTTP, TCP/IP, UPNP, DHCP, DNS, PPPOE, DDNS, FTP, P2P. |
| Mobile Phone | CamViews, (IPhone, IPad, Android) |
| Max.User Access | 10 users |
| Storage |
| Internal HDD | 1 SATA ports, up to 6TB |
| Auxiliary Interface |
| USB Interface | 2 ports, USB2.0 |
| RS485 | 1 port, For PTZ control |
| General |
| Power Supply | AHD：DC12V/2A |
| Power Consumption | <20W(without HDD) |
| Working Environment | -10 ~+55°C / 10~90%RH / 86~106kpa |
| Dimension(W*D*H) | 1U，255*244*47(mm) |
| Weight | 1.0-1.5kg(without HDD) |

Structure